## Slide 1
Is power being supplied to the switches and flip flop?
Check supply voltage and connections
Polarity right
Does Start/Stop LED work when pressed?
Check LED Polarity
Check Resistor
No
No
Resistor connected wrong
Polarity right
Switch polarity
Fix connection
Resistor grounded and connected correctly
Check continuity of Switch
Continuity good
Continuity bad
Replace switch
Yes
Yes
No
Yes
Measure flip flop with scope :
Start Q > 3.5 V
Stop: Q ~ 0V
Gates wired correctly?
Refer to datasheet for wiring
Replace Flip Flop
Yes
No
Does status LED light up when set?
Yes
Does Light sensor turn set circuit when light applied to it?
Yes
Check LED polarity
Check Resistor
Check all connections
Switch polarity
Fix Connection
Polarity wrong
Polarity wrong
Resistor not grounded and connected correctly
Resistor connected right
Check connections (diode polarity)
No
Connections right
Fix connections
Connections wrong
Calibrate potentiometer
Does thermistor reset circuit when heated with fingers?
Yes
Check connections (diode polarity)
Calibrate Potentiometer
Fix connections
Connections wrong
Connections wrong
No
Does motor run when set?
Yes
Check connections (diode polarity)
No
Does motor reset when torque is applied?
Yes
No
Circuit is Working
Check all connections
Connections right
Calibrate Potentiometer
Fix connections
Connections right